## Slide 1: A Packetized Display Protocol for Infrared Scene Projection Systems
By Aaron Landwehr
Committee:
Dr. Fouad Kiamilev, Dr. Chase Cotton,
Dr. Xiaoming Li, and Dr. Stéphane Zuckerman

## Slide 2: Background
Infrared Scene Projectors

## Slide 3: Infrared Scene Projectors (IRSP)
Used to test infrared guidance systems
Must be able to produce room-temperature and hot scenery simultaneously
Higher maximum apparent temperature is almost always better
Ideally at least as fast/high resolution as the sensors (preferably twice as big as the sensor)
Often used in real time simulations

## Slide 4: IRLED Scene Projector System
1
2
3
4
1
2
3
4
5
Scene Gen.
NUC
CSE
Dewar
RIIC
IRLED Array
SLEDS Hybrid
5
6
*
* Not Shown
drive array

## Slide 5: IRLED Scene Projector Technology Development Timeline Overview
2008 | 2011 | 2014 | 2016 | 2018
68 x 68 SLEDs array + RIIC
512 x 512 SLEDs array + RIIC +
System to drive array
System to drive SLEDs array
TCSA: Projector with 512 x 512 2-color SLEDs array
NSLEDS: Projector with 1K x 1K SLEDs array
HDILED: Projector with 2K x 2K SLEDs array

## Slide 6: SLEDs Array Pixel Ratios
HDILED
NSLEDS
TCSA
512
512
1024
1024
2048
2048

## Slide 7: Typical IRLED Projection Process
Scene-Generation
Non-Uniformity Correction/ Reordering
Digital to Analog Conversion
100hz
100hz
100hz
100hz
Projection
100hz

## Slide 8: Problem Formulation
Problem statement
Limitations
Problem Solution

## Slide 9: Problem Statement
IRSP systems need to be capable of operating at high speeds with large resolutions to meet the needs of the sensor testing community.
  High frame-rates (1Khz, 2Khz, …)
  Large resolutions (1024x1024, 2048x2048, …)
  Sub-frame latency
To reach these speeds is not possible with hardware alone.

## Slide 10: Hardware Limitations
Limitations:
  Physical Bandwidth Limitations
  Latency
  IC Clock Rates
  Analog Settling Times
  Large fanout of signals needed to drive arrays

## Slide 11: Software Limitations
Computational Limitations (Particularly with single end-points)
Algorithmic Speeds (Non-uniformity correction, etc.)
Poor optimized drivers
Lack of driver control with display protocols (fixed frame-rate, frame drops, scalability issues)

## Slide 12: Bandwidth requirements of a conventional display protocol
bandwidth | = resolution x bits x fps
bandwidth resolution bits fps | : bandwidth requirements in bits per second. : number of pixels including porches. : bits per pixel. : frames per second.

## Slide 13: Possible Solutions
Utilize Off-the-shelf Protocols:
  Take control of a complete end-to-end system.
  Off the shelf protocols and hardware.
  Develop custom hardware and software to make “off the shelf” components behave to meet system requirements.
  Limitations:
    Difficult to have low latency due to required buffering of entire frames
    Implementation and integration-costs
    System specific – upgrades or other systems require re-inventing the wheel
Design Hardware/Protocols specifically for high-speed IRLED operation Steps
  Work outside of the realm of “Display Protocols”

## Slide 14: Toward a Problem Solution
How to architect a dynamic scalable IRLED projection end-to-end system capable of
  High-performance operation  Control over bandwidth utilization and computation
  Sub-frame latency  Control synchronization
  Dynamic frame-rates  Control the sending of pixels/data
  Efficient Bandwidth utilization  Send only pixels needed
  Efficient DAC utilization  Address only pixels needed
  Upgradeability / Generalizability  Don’t tie design to specific hardware

## Slide 15: Proposed Solution: Packetized Display Protocol (PDP) Architecture
Summary:
    A physical layer agnostic method of pixel data transmission capable of providing and addressing latency guarantees while maximizing bandwidth utilization
Capable of
  Fine-grained control over frame transmission and synchronization
  Dynamic changing frame-rates from frame-to-frame
  Dynamic sub-frame framerates
  Fast decoding/processing
  Random Access Writes
Aspects
  Communication layer + Organization layer

## Slide 16: Examples of Multi-frame Rate Operation
- Red operates at 500hz - Blue operates at 20hz
High Speed
Medium Speed
Low Speed
Legend:

## Slide 17: Dynamic frame rate display with multiple regions updating at different frame rates

## Slide 18: System Overview
SLEDS
CSE
Communication Setups

## Slide 19: SLEDS System Block Diagram
Scene Generator
System
HDMI INPUT 1
HDMI INPUT 2
FPGA Main Board with 10 FMC Slots
8x DAC Cards
8x Amp Cards
2x Interface Board
Dewar – RIIC
Hybrid Array
CSE Control Box
/ NUC System
Close Support Electronics

## Slide 20: CSE External Direct Communication Block Diagram
CSE
Array
Scene Generator
CSE Operation
APIs
API Communication
Scene Generation
Scene Data
Scene Data
Signaling
LPC FMC
LPC FMC
DVI|HDMI|DP|ARNIC 818
Fiber (in development)

## Slide 21: CSE Internals

## Slide 22: CSE Externals and Empty Chassis

## Slide 23: Display Protocols
Timing
Synchronization

## Slide 24: Display Protocol Timing
VGA, HDMI, etc. Work this way.
DisplayPort Kind of works this way (more on that later).
From analog video days
Lots of time spent on blanking (more on that later)

## Slide 25: Display Protocol Timing
VGA, HDMI, etc. Work this way.
DisplayPort Kind of works this way (more on that later).
From analog video days
Lots of time spent on blanking (more on that later)

## Slide 26: Modelines (VESA Coordinated Timing)

## Slide 27: Custom Sync
Custom Sync Solution
Scene Gen.
CSE
Dewar
RIIC
IRLED Array
SLEDS Hybrid
NUC
Camera
Lack of control over Frame drops
Each component needs explicit synchronization
Often Requires Buffering Frames

## Slide 28: Packetized Display Protocol
Design Methodology
Modeline Overheads
DisplayPort Framing
Packets
PDP Overhead
Multi-frame Rate Bandwidth

## Slide 29: Design Methodology
To design a scalable display system that is distributable and hardware agnostic.
To provide a protocol that is relatively simple to implement without unnecessary complexity to ease the encoding and decoding process
To provide dynamic intra-frame variable refresh rate (VRR) in order to enable better bandwidth utilization.
To provide a path to utilize conventional display protocol streams such as HDMI as a backwards compatible transport layer for the PDP without introducing overhead

## Slide 30: Modeline Overhead
512x512 and 512x256 are typical projector system resolutions
  Not supported by VESA standard
  Does not work with all hardware
Huge for Visible Pixels vs Total Pixels
Lowering resolution increases overhead
Increasing speed with custom resolutions decreases overhead.

## Slide 31: Display Port Framing
MSA
B
S
FS
P
D
FS
P
D
FS
P
D
B
E
FE
FE
FE
P
D
F S
B
E
FE
…
…
…
…
…
MSA
B
S
Frame 1
Frame 0
Legend
Blanking Start/End
Main Stream Attribute
Pixel Data
Filling Start/End
Referred to as “packetization”
Set Types of Framing Symbols
MSA contains
  Total horizontal Pixels
  Total Lines
  Hsync/vsync information
Stuffing symbols used to space out data
Embeds formatting information into a frame.

## Slide 32: PDP Packets
Name | Type ID | Type Specific Fields |  |  |  | 
No Operation | 0x0 |  |  |  |  | 
Draw Region | 0x1 | X start | X End | Y Start | Y End | Data…
Array Reset | 0x2 | Quad |  |  |  | 
WORD sized (fixed-length decode)
  Depends on the medium
  24-bit Over HDMI
Type ID
  Packet type
Type specific fields
Draw Region
  Draws a region to the array
Array Reset
  Discharges the arrays pixels

## Slide 33: Example Stream
1
XS
XE
YS
YE
D
D
D
D
D
D
D
D
D
…
XS
XE
YS
YE
D
D
D
D
D
D
D
D
D
…
XE
YS
YE
D
D
D
D
D
D
D
D
D
…
YS
YE
D
D
D
D
D
D
D
D
…
YE
D
D
D
D
D
D
D
D
D
…
D
D
D
D
D
D
D
D
D
…
D
D
D
D
D
D
D
D
…
D
D
D
D
D
D
D
…
D
D
D
D
D
D
…
D
D
D
D
D
…
D
D
D
D
…
DR XS XE YS YE
DR XS XE YS
DR XS XE
DR XS
DR
D0 D1 D2
D0 D1
D0
DR XS XE YS YE
DR XS XE YS YE
DR XS XE YS YE
DR XS XE YS YE
D0 D1 D2 D3
Display
Stream
PDP State
Buffer
+n
DR XS XE YS YE
D4
Time
D

## Slide 34: PDP Maximum Packet Overhead
PDP Maximum Packet Overhead |  |  |  |  | 
Modeline |  | Bit-packed (13.5% Overhead) |  | Unpacked (7.2% Overhead) | 
Resolution | Framerate (Hz) | Total Pixels | Overhead Reduction (%) | Total Pixels | Overhead Reduction (%)
1920x1080 | 60 | 2397600 | 2.7 | 2235600 | 9.0
1600x1200 | 60 | 222000 | 15.4 | 2070000 | 21.7
1280x1024 | 60 | 1515520 | 13.7 | 1413120 | 20.0
1280x960 | 60 | 1420800 | 18.2 | 1324800 | 24.5
1280x800 | 60 | 1184000 | 12.9 | 1104000 | 19.2
1024x768 | 60 | 909312 | 13.9 | 847872 | 20.2
512x512 | 500 | 303104 | -2.0 | 282624 | 4.3
512x512 | 400 | 303104 | -2.0 | 282624 | 4.3
512x512 | 300 | 303104 | 13.2 | 282624 | 19.5
512x512 | 100 | 303104 | 13.2 | 282624 | 19.5
512x512 | 60 | 303104 | 13.2 | 282624 | 19.5
512x512 | 50 | 303104 | 14.5 | 282624 | 20.8
512x512 | 30 | 303104 | 36.5 | 282624 | 42.8
512x256 | 1000 | 151552 | -1.2 | 141312 | 5.1
512x256 | 500 | 151552 | 35.3 | 141312 | 41.6
512x256 | 200 | 151552 | 45.5 | 141312 | 51.8
512x256 | 100 | 151552 | 45.5 | 141312 | 51.8
512x256 | 60 | 151552 | 45.5 | 141312 | 51.8
Note: From the perspective of array writes unpacked data would only contain half the amount of “pixel” data compared to “packed” for the same modeline.

## Slide 35: Multi-frame Rate Bandwidth Savings
Bandwidth Savings relative to operating all pixels at the fast frame rate

## Slide 36: Implementation
HDMI Transport Layer / Abstract Architecture
Actual Architecture

## Slide 37: HDMI Transport Layer / Abstract Architecture
Embedding Packets

## Slide 38: HDMI as a PDP Transport
1
XS
XE
YS
YE
D
D
D
D
D
1
D
D
D
D
D
D
1
XS
XE
YS
YE
D
D
XS
XE
YS
YE
D
D
D
D
D
D
D
YS
YE
…
D
D
D
1
XS
XE
D
D
D
D
D
D
D
D
D
D
D
D
D
D
D
D
D
D
D
D
D
D
D
D
D
D
D
D
D
D
D
D
D
D
D
D
D
…
D
D
D
D
D
D
Normal HDMI Frame “Active Pixels”
Embedded PDP Frame “Active Pixels”
Map each word of a PDP packet to an HDMI 24-bit pixel word.
Decode words using fixed-width Implementation
Data locations relative to packet NOT HDMI frame.
  Type; X_Start; X_End; Y_Start; Y_End; Data…
Draw Region Packet
1
XS
XE
YS
YE
D
D
D
…

## Slide 39: Embedding PDP Packets
…
1
XS
XE
YS
YE
D
D
1
XS
XE
YS
YE
D
D
D
D
1
XS
XE
YS
YE
D
D
D
Small Data Frame (not to scale)
Large Array Emitter
High Speed
Low Speed
Low Speed
Low Speed

## Slide 40: Architecture
Abstract Architecture
Components
State Machines

## Slide 41: Abstract Architecture
Producer
Consumer
Separate domains
Classical Consumer-Producer Paradigm

## Slide 42: Overall Backend Architecture
HDMI Domain
  Synchronized Circular Buffer Write
  2 Independently Clocked Inputs
System Domain
  Synchronized Circular Buffer Read
  Array Emitter
  Write Buffer

## Slide 43: Synchronized Circular Buffer
HDMI Domain
  Write Controller
  Write Router
  Synchronized Buffer
System Domain
  Read Controller
  Read Router

## Slide 44: Synchronized Buffer

## Slide 45: Full/Empty Synchronizer
Data storage locations are synchronized using two flags
  empty_flag: when high indicates that a value has not been produced (writer clocked)
  full_flag: when high indicates that a value has been produced (reader clocked)
Usage
  Writer: stalls until the empty_flag is high, shifts in data, and toggles set_full
  Reader: stalls until the full_flag is high, shifts out data, and toggles set_empty
Operation
  Over asynchronous clock domains

## Slide 46: Memory Synchronizer Logic
Request/Acknowledgement Double Handshake Across Clock Domains
State transitions initiated via set_full and set_empty lines.
Designed so either domain can access the flags as soon as it is available
Req ↑
Ack ↑
Req ↓
Ack ↓
Read
Domain
Write
Domain
set_full
empty_flag ↓
set_empty
full_flag ↓
full_flag ↑
Stable
empty_flag ↑

## Slide 47: Two Flip-flop Synchronizer
register
register
register
bclk
aclk
data
data
data
data
Discussed in:
Clock Domain Crossing (CDC) Design & Verification Rev 1.0 Techniques Using SystemVerilog
Used to Synchronize a bit across domains
A third stage can be used for faster clocks
Ideal for FPGA based designs where timing changings by resynthesis
Bad Design to use combinational logic to route clocks

## Slide 48: Memory Synchronizer Circuit
req
register
req int
register
req
latch
ack
register
ack int
register
ack
latch
reset
reset
set
set
writer clock
reader clock
full flag
empty flag
set full
set empty

## Slide 49: Array Emitter Logic
Each controller used to decode one packet type
Controller List
  Write Enable Controller
  Reset Controller
  Valid Controller

## Slide 50: Array Emitter State Machines
Read 24-bit word and decode
State Machines
  Write Enable Controller  Draw Region State Machine
  Reset Controller  Array Reset State Machine
  Valid Controller  Not shown
Array Emitter State Machines
Data Signals
Load Pixel Data
Load Reg
Y_end
Load Reg
X_start
Load Reg
X_end
Load Reg
X_start
Write Data
Write Load=0
Write Load=1
Read Command From Data Stream
Draw Region Array Reset
1
XS
XE
YS
YE
D
D
D
…

## Slide 51: Write Buffer
Writes to an array
Inputs Muxed
Length of time per write/reset configurable
Switches between two array emitters.

## Slide 52: Experimental Results
Memory Synchronizer Testing
Firmware Characterization
High-speed & Multi-frame Rate Testing

## Slide 53: Memory Synchronizer Testing
Simulations
Experimental Testing

## Slide 54: Behavioral Simulation of a Single Pixel Being Buffered Through the Full/Empty Memory Synchronizer
Writer
Reader
Req.
Ack.

## Slide 55: Setup of Synchronizer Experiments
Test PC
ZYBO
HDMI
UART TX/RX
VGA Loop-back
Hardware
  ZYBO Test Board (Zync 7010 AP SOC)
  Intel(R) Core(TM) i7-6700 CPU @ 3.40GHz
  Nvidia M4000
  Video Capture Card
  Serial Ports (UART)
  VGA
  HDMI
Firmware (HDL)
  Synchronized Circular Buffer
  UART RX/TX Implementation
  Command Logic
  Data Verification Circuit
Software (Python)
  Based Image Driver
  Command Logic

## Slide 56: Synchronizer Experiments
R0
R1
R2
R3
R4
R5
R6
R7
R0
R1
R2
R3
R4
R5
R6
R7
Visual Test
  Send Checkerboard Image through HDMI
  Loop-back to Capture Card
  Inspect Image
Integrity Test
  Send random CRC-like patterns
  Use verification circuit to compare
  Use UART To pull statistical information and error counts.
Checkboard Image
CRC-like Random
Image
CRC-like 16-pixel Stream

## Slide 57: Simulations of Overall PDP Firmware
HDMI Input: Draw Region Packet
Array Write: From Draw Region Packet
Array Reset: From Reset Packet
HDMI IN
Write Buffer

## Slide 58: Firmware Characterization
Performed in Backwards Compatibility Mode
New PDP Firmware Vs. Old Firmware
Analog Bandwidth

## Slide 59: Grid maps
Grid with set spacing, X or Y offset each frame
Put images together & Produce Array Map
Example Input Pattern
Example Array Output

## Slide 60: Array Maps
PDP
SNAP

## Slide 61: Fractional Difference Map
PDP
SNAP

## Slide 62: Non-uniformity Corrected Image
IR
Original

## Slide 63: Analog Bandwidth
100hz
400hz
Rise Time

## Slide 64: High-speed & Multi-frame Rate Testing
Performed in PDP Mode
Select Experiments

## Slide 65: Low-speed Packetized Operation
Series of numbers operating at low speed
Demo ran from 60hz to 240hz
Used for initial verification of packetized mode of operation.
Each digit was drawn using a draw region packet

## Slide 66: One Kilohertz Operation
Moving object that bounced around the array.
Drawn using a Single Draw Region Packet.
Recorded using an IR Camera in “Windowed” Mode.
Not Possible outside of “PDP” mode of operation on the same hardware.

## Slide 67: Two Kilohertz Operation
Counting numbers
Static + Bouncing Configurations
Increments by 1 for each frame
Each digit is a separate packet.
Non-uniformity Corrected Rotating 3-dimensional Object
Maintains image fidelity
compare to 400hz bird image.
Each rotation drawn using a separate packet.

## Slide 68: Multi-frame Rate Operation
Rates:
  800hz: Bouncing Small Number
  100hz: Small Background Numbers
  2Hz: Large Number
Each Number drawn using a packet.

## Slide 69: Conclusion
Contributions
  Architected a physical layer agnostic packetized display protocol
  Architected prototype firmware that demonstrated
    backwards compatibility with existing protocols
    dynamic bandwidth utilization
    high-speed operation (2Kz, etc.)
    Demonstrated multiple Frame-rate Operation
  Used in day-to-day operations of a real system
Future Work
  Support and improve upon the technology.
  Push to see adoption within the IRSP field.
  Dynamic Frame segmentation.

## Slide 70: Done

## Slide 71: Backup

## Slide 72: Established IRSP technology
Resistor arrays (black-body emitters)
Advantages
  Well established
  Stable
  Spectrally accurate
Disadvantages
  Limited maximum temperature (~800K)
  Limited potential to scale beyond 48µm and therefore resolutions above 1024x1024
  Limited maximum speed due to cool-down
  Can be easily damaged with poorly controlled scenery
  Must be optically combined to produce separately controlled wavelengths
  Optical rise time of few milliseconds

## Slide 73: Super-Lattice Light-Emitting-Diode (SLED) based IRSP
  Very high apparent temperature (1400K+)
  High density (24µm now, 12µm or smaller in the future)
  Inherently Fast, limited primarily by the electronics
  Relatively difficult to damage thermally
  Multi-color pixels possible
  Optical rise time in nanoseconds

## Slide 74: CSE External Indirect API Communication Block Diagram
CSE
Array
Scene Generator
CSE Operation
APIs
Scene Generation
Scene Data
Scene Data
Signaling
CSE Operations Box
Client
Comm
Serial
Comm
LPC FMC
LPC FMC
DVI|HDMI|DP|ARNIC 818
Fiber (in development)

## Slide 75: CSE External Indirect API and Data Communication Block Diagram
CSE
Array
Scene Generator
CSE Operation
APIs
Scene Generation
Scene Data
Scene Data
Signaling
CSE Operations Box
Client
Comm
Serial
Comm
LPC FMC
LPC FMC
DVI|HDMI|DP|ARNIC 818
Fiber (in development)
Scene Data
Scene Data
Pre-formatted

## Slide 76: Horizontal Cross Section Timing

## Slide 77: Full Cross Section Timing

## Slide 78: Formulas

## Slide 79: PDP Overhead
Maximum Packet Count
Total Pixel Count with Overhead
Minimum Packet Size
Resolution
Packet Overhead
Total Pixel Overhead
Draw Region Packet size
Minimum Region Write Size
(bit-packed)
Minimum Region Write Size
(unpacked)

## Slide 80
PDP Overhead Percentage
Total Overhead Percentage
Overhead (bit-packed)
Overhead (unpacked)
Total Pixel Overhead
Total Pixel Count with Overhead

## Slide 81: Frontend Architecture
Communication
APIs

## Slide 82: C Implementation
Interface Board
Interface Board
SuperFPGA
NUCPC
Frontend
Firmware /
MicroBlaze
Controller
Backend
Firmware /
FPGA
Master
Microcontroller
Slave
Microcontroller
LCD
Command Based Two-sided Communication between Frontend PC and Frontend Firmware
Used to control the firmware settings and mode of operation
Twiddles Memory Mapped Registers

## Slide 83: Select Frontend APIs
Remote RPC Layer (zerorpc)
Callable APIs

## Slide 84: Full/Empty Memory Synchronizer State Transitions
Signal | Stable  |  |  | S e t | Wr Domain  Rd Domain |  |  | Stable |  |  | S e t | Rd Domain  Wr Domain |  |  |  | Wr Domain  Rd Domain |  |  |  | Rd Domain  Wr Domain |  |  | Stable |  | 
set_full | 0 | … | 0 | 1 | 0 | … | 0 | 0 | … | 0 | 0 | 0 | … | 0 | 0 | 0 | … | 0 | 0 | 0 | … | 0 | 0 | … | 0
set_empty | 0 | … | 0 | 0 | 0 | … | 0 | 0 | … | 0 | 1 | 0 | … | 0 | 0 | 0 | … | 0 | 0 | 0 | … | 0 | 0 | … | 0
req latch | 0 | … | 0 | 0 | 1 | … | 1 | 1 | … | 1 | 1 | 1 | … | 1 | 1 | 0 | … | 0 | 0 | 0 | … | 0 | 0 | … | 0
req int reg | 0 | … | 0 | 0 | 0 | … | 1 | 1 | … | 1 | 1 | 1 | … | 1 | 1 | 1 | … | 0 | 0 | 0 | … | 0 | 0 | … | 0
req reg | 0 | … | 0 | 0 | 0 | … | 0 | 1 | … | 1 | 1 | 1 | … | 1 | 1 | 1 | … | 1 | 0 | 0 | … | 0 | 0 | … | 0
ack latch | 0 | … | 0 | 0 | 0 | … | 0 | 0 | … | 0 | 0 | 1 | … | 1 | 1 | 1 | … | 1 | 1 | 0 | … | 0 | 0 | … | 0
ack int reg | 0 | … | 0 | 0 | 0 | … | 0 | 0 | … | 0 | 0 | 0 | … | 1 | 1 | 1 | … | 1 | 1 | 1 | … | 0 | 0 | … | 0
ack reg | 0 | … | 0 | 0 | 0 | … | 0 | 0 | … | 0 | 0 | 0 | … | 0 | 1 | 1 |  | 1 | 1 | 1 | … | 1 | 0 | … | 0
empty flag | 1 | … | 1 | 1 | 0 | … | 0 | 0 | … | 0 | 0 | 0 | … | 0 | 0 | 0 | … | 0 | 0 | 0 | … | 0 | 1 | … | 1
full flag | 0 | … | 0 | 0 | 0 | … | 0 | 1 | … | 1 | 1 | 0 | … | 0 | 0 | 0 | … | 0 | 0 | 0 | … | 0 | 0 | … | 0

## Slide 85: Behavioral Simulation of Multiple Pixels Being Buffered Through the Full/Empty Memory Synchronizer
Req.
Ack.
Writer
Reader

## Slide 86: Array Write Process
Array Layout
Pixel Layout
Array Write Process
Data Processing & Ordering

## Slide 87: TCSA, NSLEDS, and HDILED Array Quadrant Layouts
NSLEDS
HDILED
Q1
Q2
Q3
Q4
1024
1024
512
512
Q1
Q2
Q3
Q4
2048
1024
1024
2048
Q1
Q2
Q3
Q4
512
256
256
512
TCSA

## Slide 88: NSLEDS/HDILED Array Super Pixel Layout
0 1 2 3 4 5 6 7
0
1
2
3
4
5
6
7
Rows
Columns
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
p|ch1
p|ch1
n|ch0
n|ch0
LOAD=0
LOAD=1
Shared Drive Strength
Shared Drive Strength
Tiled Super Pixels
Super Pixels

## Slide 89: Interleaved Array Write Process
Buffer 32 pixels worth of data.

## Slide 90: Bit-packing Format
RGB Legend
R: Red G: Green B: Blue
Mapping Legend
S: Drive Strength L: Left R: Right U: Unused
11
11
1
Bit | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
RGB | R | R | R | R | R | R | R | R | G | G | G | G | G | G | G | G | B | B | B | B | B | B | B | B
Mapping | S | L | L | L | L | L | L | L | L | L | L | L | U | R | R | R | R | R | R | R | R | R | R | R
Pixel Data Bit-packing
“Pixels” are clipped and scaled into an 11-bit format packeted into a 24-bit RGB pixel word.
Segmented by column
  Even columns go into the L portions.
  Odd Columns go into the R portions.
For example:
  Pixels of column 0 and 1 would combine into a single 22-bit RGB pixel (with one strong bit).
  Pixels of Column 2 and 3 would combine similarly, so on so forth

## Slide 91: Image Processing
Original or NUC Image
Bit-pack
Even/Odd Row Reorder
Transpose
Array
CSE Input 1
CSE Input 2
*Not Accurate Out, For Explanation Only
*

## Slide 92: Quadrant Layout
Q2
Q1
Q3
Q4
Q2
Q1
Q3
Q4
Q1
Q2
Q3
Q4
Q1
Q2
Q3
Q4
Q1
Q2
Q3
Q4
*Not Accurate Out, For Explanation Only
*

## Slide 93: Quadrant Layout Colored
Original or NUC Image
Bit-pack
Even/Odd
Row Reorder
Transpose
Array
Q1
Q2
Q4
Q3
Q4
Q3
Q1
Q2
Q4
Q3
Q1
Q2
Q4
Q3
Q1
Q2
Q1
Q2
Q4
Q3
*Not Accurate Out, For Explanation Only
*

## Slide 94: Bit-packing
Original or NUC Image
Bit-pack
Even/Odd Row Reorder
Transpose
Array
0 1 2 3 4 5
0 1 2
*Not Accurate Out, For Explanation Only
*
Clip & scale pixels down to 11 bits each, pack two 11-bit pixels into one 24-bit pixel.

## Slide 95: Data Reordering
Original or NUC Image
Bit-pack
Even/Odd
Row Reorder
Transpose
Array
0
63
31
32
0
63
31
32
1024
1024
512
512
512
1024
*Not Accurate Out, For Explanation Only
*
16 even, 16 odd, 16 even, 16 odd…

## Slide 96: Example 1
Original or NUC Image
Bit-pack
Even/Odd Row Reorder
Transpose
Array
CSE Input 1
CSE Input 2
*Not Accurate Out, For Explanation Only
*

## Slide 97: Example 2
Original or NUC Image
Bit-pack
Even/Odd
Row Reorder
Transpose
Array
CSE Input 1
CSE Input 2
*Not Accurate Out, For Explanation Only
*

## Slide 98: Example 3
Original or NUC Image
Bit-pack
Even/Odd Row Reorder
\
Transpose
Array
CSE Input 1
CSE Input 2
*Not Accurate Out, For Explanation Only
*

## Slide 99: Example IR
Original or NUC Image
Bit-pack
Even/Odd Row Reorder
Transpose
Array
CSE Input 1
CSE Input 2

## Slide 100: Example IR 2
Original or NUC Image
Bit-pack
Even/Odd Row Reorder
Transpose
Array
CSE Input 1
CSE Input 2

## Slide 101: Machine Model
Abstract Machine Model
Compositing Example

## Slide 102: Hardware Mapping of an IRLED Projection Process
NUC Hardware
Array
CSE
Sc. Gen. Hardware
Scene-Generation
Non-Uniformity Correction / Reordering
Digital to Analog Conversion
Projection
Array
CSE
Sc. Gen. Hardware
Scene-Generation
Non-Uniformity Correction / Reordering
Digital to Analog Conversion
Projection

## Slide 103: Abstract Machine Model
Component breakdown:
  1 to N Scene Generators
  1 to M Compositors
  1 to P Projector Tiles
Benefits
  Scalability
  Distributed
  Generalizable

## Slide 104: Compositing PDP
Composite frames and segmenting them
  Change delta of frames
  Relying on scene-generator to provide annotated priorities

## Slide 105: Composited Together
High Speed
Medium Speed
Low Speed
Legend:
Video of Data (generated in parts or as a whole)
Segment frames into sub-frames
Each with variable frame operation

## Slide 106: Prioritization
High changes in intensity give high priority.